## Slide 1: Hard Hats Detection in Unmanned Factory 無人廠房安全帽檢查
@Peter Chang peter8606@gmail.com
https://github.com/wildman8606/ARC_EM9D_AIoT_DK/

## Slide 2: I. Introduction I-1. Abstract
The failure of factory personnel to wear safety equipment as required is one of the main causes of serious injuries. In order to avoid tragedies, this research uses human detection and object recognition technology to determine whether workers are wearing safety helmet as required when entering the construction site, so as to achieve automated safety inspections.
Define the detection Region of Interest (ROI) in the aisle image. When the worker enters the area of interest, the system starts to detect the person on the screen and obtain the image for detection. The detection result uses a light signal to show whether it meets the standard.
Fig. 1. Must wear a safety helmet
when entering the factory.
Fig. 2. The detection of whether
wearing safety helmets

## Slide 3: I. Introduction I-2. Situational Simulation
Situational Example.
Alert
PASS
Fig.3. Detecting safety helmet simulation

## Slide 4: I. Introduction I-3. ARC EM9D AIoT DK
Signal LEDs
Fig. 4 Hard Hats Detection in Unmanned Factory
EM9D
Button

## Slide 5: I. Introduction I-4. Flow Chart –user flow
Fig. 5 user case flow.
Human Passing?
Camera Get Image
Photoelectric Switch Check Region of Interest
T
F
Model
Inference
Safety Helmet?
Correct signal
Warning
signal
T
F

## Slide 6: II. Implement II-1. Get Training Dataset
Step1: Download [Synopsys_SDK_V21] file
Step2: Enter folder [Lab3_Camera_v0] and make
$ cd \Synopsys_SDK_V21\Source_Project\Lab3_Camera_v0
$ make clean
$ make
$ make flash
Step3: In [Synopsys_SDK_V21\tools\image_gen_cstm\output]
folder find [output.img] file and copy

## Slide 7: II. Implement II-1. Get Training Dataset
Step4: Short J20 and J11 for update application mode
Step5: Use[Synopsys_SDK_V21\tools\HMX_FT4222H_GUI\GUI_binary \
HMX_FT4222H_GUI.exe]tool and download image file to CPU
Step6: Open J20 for run mode
Step7: Press reset button SW4. MCU will reset and run the application
J20
J11
Step6:
Step4:

## Slide 8: II. Implement II-1. Get Training Dataset
Step8: Open the terminal log to record and output RAW image data.
Step9: After key in “A”, WE I start to capture and send image data.
Fig. 7 Use the terminal to output log

## Slide 9: II. Implement II-1. Get Training Dataset
Step10: Delete irrelevant content in logs
Delete
Fig. 8 Delete and only save the image part

## Slide 10: II. Implement II-1. Get Training Dataset
Step11: Copy log file to [Synopsys_SDK_V21\Example_Project\LabPY_raw2png]
Step12: Rename log file to "camera_y.log"
Step13: Open "./LabPY_raw2png/raw2png.ipynb" with Jupyter Notebook
Step14: Run and get "my_gray.png"

## Slide 11: II. Implement II-2. Data Augmentation
In the real world scenario, we may have a dataset of images taken in a limited set of conditions. But our target application may exist in a variety of conditions, such as different orientation, location, scale, brightness etc. We account for these situations by training our neural network with additional synthetically modified data.
Data
Augmentation
Fig. 10 Data Augmentation

## Slide 12: II. Implement II-2. Data Augmentation
>>> import augly.image as imaugs
>>> image = imaugs.blur(aug_image,output_path=path) #模糊
>>> image = imaugs.random_noise(aug_image,output_path=path) #隨機噪聲
>>> image = imaugs.hflip(aug_image,output_path=path) #水平翻轉
>>> image = imaugs.vflip(aug_image,output_path=path) #垂直翻轉
>>> image = imaugs.brightness(aug_image,factor=random.uniform(0.1, 2),output_path=path) # 亮度
>>> image = imaugs.rotate(aug_image,degrees=random.uniform(1, 10),output_path=path) #旋轉
>>> image = imaugs.sharpen(aug_image,factor=random.uniform(5, 20),output_path=path) #銳化

## Slide 13: II. Implement II-2. Model Building
model=Sequential()
model.add(Conv2D(filters=96,
kernel_size=(filter_x, filter_y),
padding="same",
input_shape=input_shape))
model.add(BatchNormalization())
model.add(Activation("tanh"))
model.add(MaxPooling2D())
model.add(Conv2D(filters=192,
kernel_size=(filter_x, filter_y),
padding="same",
input_shape=input_shape))
model.add(BatchNormalization())
model.add(Activation("tanh"))
model.add(MaxPooling2D())
model.add(Flatten())
model.add(Dense(384))
model.add(BatchNormalization())
model.add(Activation("tanh"))
model.add(Flatten())
model.add(Dense(32))
model.add(BatchNormalization())
model.add(Activation("tanh"))
model.add(Dense(num_classes))
model.add(Activation("softmax"))
print(model.summary())

## Slide 14: II. Implement II-2. Model Building

## Slide 15: II. Implement II-2. Model Training
>>> lr_reducer = ReduceLROnPlateau(monitor=‘loss’, factor=np.sqrt(0.1), verbose=1, cooldown=1, patience=3, min_lr=1e-10)
>>> earlystop = EarlyStopping(monitor='val_loss', min_delta=0, patience=7, verbose=0, mode='auto', baseline=None, restore_best_weights=False)
>>> callbacks = [lr_reducer, earlystop]
>>> print('starting training....')
>>> history = model.fit(x_train,y_train,
batch_size=batch_size,
epochs=epochs,
validation_split=0.1,
shuffle=True,
verbose=1,
callbacks=callbacks)

## Slide 16: II. Implement II-2. Model Check
Can pip install netron ,and check model structure.
Fig. 13 Use netron.app can see model structure.

## Slide 17: II. Implement II-2. TFLiteConvert
>>> converter = tf.lite.TFLiteConverter.from_keras_model(model)
>>> converter.optimizations = [tf.lite.Optimize.DEFAULT]
>>> converter.target_spec.supported_ops = [tf.lite.OpsSet.TFLITE_BUILTINS_INT8]
>>> converter.inference_input_type = tf.int8
>>> converter.inference_output_type = tf.int8
>>> tflite_model = converter.convert()
>>> preprocessed_test_images = tf.cast(train_images, tf.float32)
>>> emnist_ds = tf.data.Dataset.from_tensor_slices((preprocessed_test_images)).batch(1) #construct a dataset
>>> def representative_data_gen():
>>> for input_value in emnist_ds.take(100):
>>> yield [input_value]
>>> converter.representative_dataset = representative_data_gen
>>> import pathlib
>>> converted_model = converter.convert()
>>> generated_dir = pathlib.Path("generated/")
>>> generated_dir.mkdir(exist_ok=True, parents=True)
>>> converted_model_file = generated_dir/"model.tflite"
>>> converted_model_file.write_bytes(converted_model)

## Slide 18: II. Implement II-2. TFLiteConvert

## Slide 19: II. Implement II-2. Create .img
Step1: In order to integrate converted model into TFLM application we
have to save it as a C array.
$ xxd -i model.tflite > model.h
Step2: Copy " model.h " to " Example_Project\Lab5_tflm_emnist_letter "
Step3: Set model setting in " model settings.cpp " and " model settings.h "
Step4: Edit micro_op_resolver for your model in " tflitemicro_algo cpp "
Step5: Edit TensorFlow input and output buffer in " tflitemicro_algo cpp “
Step6: make files
$ make clean
$ make
$ make flash

## Slide 20: III. Implement III-2. Create .img
Fig. 15 Make and create .img flile.

## Slide 21: II. Implement II-3. Upload CPU
Step1: Open the [HMX_FT4222H_GUI.exe].
Step2: Push the [Read ID]button,and to check it shows [ef/60/15].
Step3: Push the [Chip Erase]button.
Step4: Choose the file location and press the [Programing] button.
Step5: Power off ,and open J20 for run mode

## Slide 22: II. Implement II-3. Upload CPU

## Slide 23: II. Implement II-4. Runtime

## Slide 24: II. Implement II-4. Runtime

## Slide 25: II. Implement II-4. Runtime
When it is detected that you are wearing Hard Hats , the green signal light will be displayed, otherwise it will be red. The button is a digital input and can also be replaced by a photoelectric switch

## Slide 26: III. Suggeestions
1. Increase chip memory size.
2. Increase the pixels and replace the RGB camera.
3. When taking training photos, I hope to output to the SD card module, not the uart print display.